## Slide 2
DTS Self-Lining / Self-Expansion Process is Unrelated to Yielded Expansion
Two DTS Technology Forms:
Interleaving, laminated tubular-spring provides pressure compliance
Porous helical lattice arrangements as high permeability sandscreens
Expansion Ratios >3X, Self-Sealing Pressure >10ksi
Expanded Form is the Natural Condition, Setting Forces are Tunable
Deployable by CT or Wireline
>50 Applications Covering D&C, Interventions, P&A
  Current emphasis on thru-tubing applications
Elastic Phase Self-Lining Tubulars Resolve Limitations of Inflatable, Swellable, and Expandable Technologies
Increased Production │ Reduced Well Cost │ Target Depth Assurance │ Wellbore Integrity

## Slide 3
Mechanical Performance Correlates with High Strength Material Construction
Yield strengths typically >200ksi
Hardness normally >50Rc, abrasion resistance is inherent
Low D:t <10, high strength steel / high expansion ratios capable
Burst and Collapse Properties are Approximately Equal
Certain Assemblies are Retrievable or Positionally Adjustable
DTS Thru-Tubing Solutions are Large Bore & Monodiameter Capable
  Repaired ID allows subsequent repairs below
High Permeability Relining Screens for Compromised Sandcontrol
• Thru-tubing Capable
• Industry Best Sand Control Integral
• High Rate Capable
• Erosion Resistant
• Plug Resistant, Thorough Jetting Capable
High Strength Liners &
Claddings, Expansion >3X
Increased Production │ Reduced Well Cost │ Target Depth Assurance │ Wellbore Integrity
Technology Features

## Slide 4
Increased Production │ Reduced Well Cost │ Target Depth Assurance │ Wellbore Integrity
Form Oversized Split Tubes from High
Strength Plate.
Assemble & Join Members as a
Diametrically Oversized Spring-Tubular:
  – Laminated assembly
Temporarily Reduce Diameter & Secure
RIH, Release Elastically Biased Assembly
to its Operating Diameter.
Seal Wellbore By Residual Outward Spring Energy
  – Self-hanging and self-sealing
‘Solids’ ─ Elastic Expansion Technology Principles
Process Is Fundamentally Opposite Yielded Expansion

## Slide 5
3” OD Solid Liner Passed Through 4.5” Tubing, Set Capable >8.5”
http://dynamictubulars.com/high_speed_lab_film.htm

## Slide 6
CT or Wireline
Production Tubing
Pre-Expansion Clad, Patch or Sand Relining
LARGE BORE THRU-TUBING ISOLATION, PATCH OR SAND RELINING RUNNING PROCEDURE
Maximum Post-Intervention
OD & ID:
Maximized Post-Set ID Enables Access For Subsequent Linings
Relining Lowered To Target Zone, Pressure or Electro-Mechanical Force Initiates Expansion
Self-Biasing Against Casing or Screen

## Slide 7
Increased Production │ Reduced Well Cost │ Target Depth Assurance │ Wellbore Integrity
Uses of Full Access Thru-tubing, FATTCladding©
Water or gas shutoff against casing
More timely & reliable alternative to cement or chemical treatments
Isolation, pre-stimulation and/or post-stimulation
Thin-walled / high-strength tubing patches
Uses Under Consideration
Diversion of hotspots by scab liner set against screen
Partial water shutoff as scab liner set against screen
Sand shutoff as scab liner set against screen
Bridging / straddle conduit between short height chemical, solder or
cement treatments.
Radial / internal support of chemical, solder or cement treatments
behind pipe.

## Slide 9
Thin Walled Tubing Patch Dimensions, >200ksi Materials
<.100” Wall Thickness Table Also Available.

## Slide 10
Increased Production │ Reduced Well Cost │ Target Depth Assurance │ Wellbore Integrity
Full Diameter Maintenance Field Demonstrations
Thru-tubing RIH Diameter Isolation Set In Upper Section, 4-1/2” Casing.
Thru-tubing RIH Diameter Sand Reline Set In Lower Section, 4-1/2” Casing.

## Slide 11
Self-lines fully against existing screen or
casing, maximizing producible OD and ID.
5X – 10X more plug resistant than any sand
device & can be thoroughly jetted.
Manufactured from high strength, erosion resistant materials, to ceramic levels.
Unlimited system permeability is conducive
to high rate well production.
“DTSS” Thru-tubing Relining Screens for Failed Sandcontrol
Increased Production │ Reduced Well Cost │ Target Depth Assurance │ Wellbore Integrity

## Slide 12
Increased Production │ Reduced Well Cost │ Target Depth Assurance │ Wellbore Integrity
DTS Lattice Sandscreen ― Oversized Diameters Built From High Strength Spring Elements
5. Excess Spring Energy Supports Wellbore
1. Temporary, Elastically Reduced
RIH Diameter. Secured.
2. Internal Pressure Applied,
Temporary Constraints Released.
Oversized Diameter, As Manufactured
3. Recovering Biased-Oversizing
4. Intended Operating Diameter

## Slide 13
Increased Production │ Reduced Well Cost │ Target Depth Assurance │ Wellbore Integrity
Sandcontrol reline remediating normal wear, GP unnecessary
Reline high erosion / compromised frac pack hotspots, no GP
Plug prone environments requiring jetting efficacy
Diameter constrained interventions / recompletions
Low pressure isolation sleeves
Slidable or retrievable hybrid
sleeves & screens.
Uses of Large Bore Thru-tubing Sand Relining

## Slide 14
2.5X Expansion, Elastically Compressed and Recovered 2:1 Opening:Strainer Arrangement.

## Slide 15
Initial Standard Well Construction Test Results, Ideal Expanded Sandscreen Properties of Shell & BP Exceeded:
Ideals Industry Standard DTS Capability
A. Expansion Ratio 125%–150% Originally ~116% >170%
B. Ultimate Collapse Rating >2000-psi Originally 250-psi >8,000-psi
C. Flexible Formation Bias-Support 200-psi Unspecified >1,000-psi
D. Axially Subsiding Compliance 10% Non-existent 6%, >10%
E. Net Inflow, Open Area Maximize <12% 60%
F. Mesh Particle Size Retention 50µ – 250µ >125µ >25µ
G. Flow-Area % At Pre-expansion
Min. Intervention Diameter: Maximize Non-existent 20%
Increased Production │ Reduced Well Cost │ Target Depth Assurance │ Wellbore Integrity
Notes: Describe the technology, secret sauce or magic behind your product. The less text and the more diagrams, schematics and flowcharts, the better. If you have a prototype or demo, this is the time to transition to it. As Glen Shires of Google said: “If a problem is worth 1000 words, a prototype is worth 10 000 slides.”